## Slide 1: WF on remaining PHR aspects for dual connectivity
NTT DOCOMO, Nokia Networks, Nokia Corporation
R1-143440
3GPP TSG RAN WG1 #78
Dresden, Germany, 18th – 22nd August 2014
Agenda item 7.2.2

## Slide 2: Proposals (1)
PHR is computed before per-CC power-scaling (if any) as in Rel.8-11.
In asynchronous dual connectivity, PHR of the serving cells belonging to non-scheduling eNB is calculated using the first overlapped portion.

## Slide 3: Proposals (2)
PCMAX is not reported by the PHR MAC CE in Rel.12 dual connectivity, as in Rel.10-11 CA.
When the UE is configured with “always virtual PH”,
  The “V” field of the serving cell c which belongs to non-scheduling eNB is fixed to 1.
  PCMAX,c of the serving cell c which belongs to non-scheduling eNB is not reported.
Confirm the PHR reporting procedures summarized in R1-143245.
  See the next slides.

## Slide 4: When “Always virtual PH” is configured
 | PH calculation for serving cells belonging to MCG/MeNB | PH calculation for serving cells belonging to SCG/SeNB
PHR sent to MeNB | Rel.11 PHR procedures apply If simultaneous PUSCH/PUCCH transmission is configured within the CG, then type 2 PHR is configured for PCell | Type 1 and 2 PHs of pSCell are always reported Type 1 PHs of other cells than pSCell of SCG are included in the PHR Type 1 PH is computed using Rel.11 equation for which the UE does not transmit PUSCH for serving cell Type 2 PH is computed using Rel.11 equation for which the UE does not transmit PUCCH or PUSCH for the serving cell (i.e. pSCell)
PHR sent to SeNB | Type 1 and 2 PHs of PCell are always reported Type 1 PHs of other cells than PCell of MCG are included in the PHR Type 1 PH is computed using Rel.11 equation for which the UE does not transmit PUSCH for the serving cell Type 2 PH is computed using Rel.11 equation for which the UE does not transmit PUCCH or PUSCH for the serving cell (i.e. PCell) | Rel.11 PHR procedures apply If simultaneous PUSCH/PUCCH transmission is configured within the CG, then type 2 PHR is configured for pSCell

## Slide 5: When “Always virtual PH” is NOT configured
 | PH calculation for serving cells belonging to MCG/MeNB | PH calculation for serving cells belonging to SCG/SeNB
PHR sent to MeNB | Rel.11 PHR procedures apply If simultaneous PUSCH/PUCCH transmission is configured within the CG, then type 2 PHR is configured for PCell | Type 1 and 2 PHs of pSCell are always reported Type 1 PHs of other cells than pSCell of SCG are included in the PHR Rel.11 PHR procedures apply
PHR sent to SeNB | Type 1 and 2 PHs of PCell are always reported Type 1 PHs of other cells than PCell of MCG are included in the PHR Rel.11 PHR procedures apply | Rel.11 PHR procedures apply If simultaneous PUSCH/PUCCH transmission is configured within the CG, then type 2 PHR is configured for pSCell