## Slide 1: WF on SCell PUCCH mechanisms in CA
NTT DOCOMO, NEC, Hitachi
R1-143441
3GPP TSG RAN WG1 #78
Dresden, Germany, 18th – 22nd August 2014
Agenda item 7.2.2

## Slide 2: Background
PUCCH transmission on two serving cells in CA is realized by:
  Two cell-groups are configured for the UE.
  One SCell carrying PUCCH is configured in the cell-group that does not contain PCell for the UE.
  No cross-carrier scheduling across cell-groups.
Above is exactly same as dual connectivity from a physical layer viewpoint.

## Slide 3: Proposals (1)
No new UCI multiplexing mechanisms other than those for dual connectivity is introduced.
  When a UE is configured with PUCCH on SCell for CA, UCI multiplexing is carried out per cell-group, as in dual connectivity.
No new power control mechanisms other than those for dual connectivity is introduced.
  When a UE is configured with PUCCH on SCell for CA, power control of PUCCH on SCell follows PSCell PUCCH power control in dual connectivity.

## Slide 4: Proposals (2)
DCI format 3/3A is not supported for PUCCH carried by SCell in CA.