## Slide 1: Way Forward on 256QAM Design
Huawei, HiSilicon, CMCC, Samsung, CATT, CATR
3GPP TSG RAN WG1 Meeting #78 R1-143467
Dresden, Germany, 18th - 22th August 2014
Agenda Item: 7.2.1.1

## Slide 2: Proposal for 256QAM CQI table
Confirm the working assumption of 256QAM CQI table
  Following CQI table is applied for 256QAM
CQI index | modulation | code rate x 1024 | efficiency
0 | out of range |  | 
1 | QPSK | 78 | 0.1523
2 | QPSK | 193 | 0.3770
3 | QPSK | 449 | 0.8770
4 | 16QAM | 378 | 1.4766
5 | 16QAM | 490 | 1.9141
6 | 16QAM | 616 | 2.4063
7 | 64QAM | 466 | 2.7305
8 | 64QAM | 567 | 3.3223
9 | 64QAM | 666 | 3.9023
10 | 64QAM | 772 | 4.5234
11 | 64QAM | 873 | 5.1152
12 | 256QAM | 711 | 5.5547
13 | 256QAM | 797 | 6.2266
14 | 256QAM | 885 | 6.9141
15 | 256QAM | 948 | 7.4063

## Slide 3: Proposal for 256QAM MCS table
Confirm the working assumption of 256QAM MCS table
  Not to additionally remove any other MCS entry or entries
  Positions of MCS indices are ordered based on spectral efficiency
  Following MCS table is applied to 256QAM
MCS Index | Modulation Order | TBS Index
0 | 2 | 0
1 | 2 | 2
2 | 2 | 4
3 | 2 | 6
4 | 2 | 8
5 | 4 | 10
6 | 4 | 11
7 | 4 | 12
8 | 4 | 13
9 | 4 | 14
10 | 4 | 15
11 | 6 | 16
12 | 6 | 17
13 | 6 | 18
14 | 6 | 19
15 | 6 | 20
16 | 6 | 21
17 | 6 | 22
18 | 6 | 23
19 | 6 | 24
20 | 6 | 25
21 | 8 | 27
22 | 8 | 28
23 | 8 | 29
24 | 8 | 30
25 | 8 | 31
26 | 8 | 32
27 | 8 | 33
28 | 2 | Reserved
29 | 4 | 
30 | 6 | 
31 | 8 | 

## Slide 4: Proposal for 256QAM TBS table
Confirm the working assumption of 256QAM TBS table in R1-142735
Down-select the FFS values in Dresden meeting between
  Option1
  Option2
TBS_L2 | TBS_L3 | TBS_L4
193768 | 290664 | 387560
TBS_L2 | TBS_L3 | TBS_L4
195816 | 293736 | 391656

## Slide 5: Proposal for 256QAM configuration
Confirm the working assumption
  for TM10, CQI table are common for all CSI processes and/or Rel-11 subframe measurement sets and MCS table is common for all PQI sets
  for TM1-9, 256QAM CQI table can be configured per each Rel-11 subframe measurement set

## Slide 6: Proposal for 256QAM configuration
Down-select the MCS configuration for Rel-11 subframe set in TM1~9 in Dresden meeting among
  Option1: For TM1~9, a single MCS table is applied for all the subframes. If at least one of the measurements subframe set is configured with the 256QAM CQI table, the UE assumes the 256QAM MCS table.
  Option2: For TM1~9, one MCS table can be configured for each Rel-11 subframe measurement set, which corresponds to the CQI table in the same subframe set.
    Option2a: for subframes that do not belong to either subframe set, legacy MCS table is assumed at the UE
    Option2b: for subframes that do not belong to either subframe set, the same MCS table as subframe set 0 or 1 is assumed at the UE
  Option3: For TM1~9, a single MCS table is applied for all the subframes, which is independent of the measurement subframe set specific CQI configuration (i.e. a single MCS table is configured for TM1~10)
    The following configurations are allowed
CQI table configuration for csi-MeasSubframeSet1-r10 | CQI table configuration for csi-MeasSubframeSet2-r10 | MCS table configuration for all the subframes
256QAM CQI table | legacy CQI table | 256QAM MCS table
legacy CQI table | 256QAM CQI table | 256QAM MCS table
256QAM CQI table | 256QAM CQI table | 256QAM MCS table
legacy CQI table | legacy CQI table | legacy MCS table
CQI table configuration for csi-MeasSubframeSet1-r10 | CQI table configuration for csi-MeasSubframeSet2-r10 | MCS table configuration for all the subframes
256QAM CQI table | legacy CQI table | 256QAM or legacy MCS table
legacy CQI table | 256QAM CQI table | 256QAM or legacy MCS table
256QAM CQI table | 256QAM CQI table | 256QAM MCS table
legacy CQI table | legacy CQI table | legacy MCS table