## Slide 1: Way-forward on NAICS fallback
CATT, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Ericsson, Nokia Corporation, Nokia Networks,
3GPP TSG RAN WG1 #78
Dresden, Germany, 18th – 22nd August 2014
Agenda item 7.2.4.2
R1-143528

## Slide 2: Background
NAICS performance gain is shown in RAN4 when neighbor cell interference is fixed and aligned with the RRC-configured subset
  RAN4 also assume fixed MCS/RI interference modeling
  Strict eNB scheduling restriction is implied
eNB scheduling however is dynamic and cannot be mandated to follow the restricted parameter subset
  Cell load, user arrival, data package, are all dynamic
Certain interference cannot be handled by NAICS UE (e.g. distributed VRB, DCI 1A triggered PDSCH in 4-port cell)
  NAICS simulation in RAN4 has not taken into account such interference scenario
Worse performance than MMSE-IRC is possible, unless eNB has a mechanism to turn OFF NAICS more flexibly (e.g. fallback)

## Slide 3: Proposal
It is RAN1’s understanding that RAN4 will include test cases that guarantee that NAICS UE does not perform worse than Rel-11 MMSE-IRC even when configured subset restrictions are not applied and when interference not supported by NAICS is present (e.g. DVRB, precoding granularity) at cells/TPs for which NAICS assistance signaling is provided.