## Slide 1: WF on multiple discovery resource pools
Samsung, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, LGE
3GPP TSG RAN WG1 #78bis R1-144372
Ljubljana, Slovenia
6th – 10th October 2014
A.I. 7.2.1.3

## Slide 2: Background
Agreement In RAN1 #78
  From the UE perspective, at any given time instant, up to 4 discovery transmission pools can be independently configured, each of which may be configured for either of the discovery types

## Slide 3: Proposal
  More than 1 resource pools are supported for type-1 discovery resource pool configuration
  There are more than 1 resource pools for discovery signal transmission
  A UE selects its resource pool for discovery signal transmission based on UE RSRP measurement, DL path-loss, or Tx power.
  Resources for each resource pool and RSRP threshold (or DL Path-loss/Tx power threshold) are configured by the network