## Slide 1: WF on UE complexity reduction for MTC
Ericsson
R1-144433
3GPP TSG RAN WG1 #78bis
Ljubljana, Slovenia, 6th – 10th October 2014
Agenda item 7.3.1.1.1

## Slide 2: Proposal
Agreements
  Reduced UE bandwidth of 1.4 MHz in downlink and uplink is prioritized as the most important complexity reduction technique for Rel-13 MTC UEs.
  Send LS to RAN4 on e.g. re-tuning time and maximum transmission power at RAN1#79.
Working assumptions
  The maximum TBS for unicast transmission for Rel-13 low complexity UE is 1000 bits.
  The maximum TBS for broadcast transmission for Rel-13 low complexity UE is 1000 bits.
  No simultaneous reception of multiple transmissions for Rel-13 low complexity UE or enhanced coverage UE.