## Slide 1: Proposals on SRS handling in dual connectivity
NTT DOCOMO
R1-144446
3GPP TSG RAN WG1 #78bis
Ljubljana, Slovenia, 6th – 10th October 2014
Agenda item 7.2.2.1

## Slide 2: Background
RAN1 agreed following TPC rules for PUCCH/PUSCH
  DC power-control mode 1
    Guaranteed power is configured per cell-group
      But all the transmit power can be shared b/w CGs
    Remaining power is utilized based on UCI priority rule
  DC power-control mode 2
    Guaranteed power is configured per cell-group
      It is not usable by the other CG if there is a potential UL tx
    Remaining power is utilized based on earlier tx priority

## Slide 3: Proposal (1)
If the transmit power of PUCCH/PUSCH/SRS of a CG is equal to or lower than a guaranteed power configured for the CG, the transmit power is guaranteed
  Except when it is overlapped with a PRACH in the other CG and the UE is power-limited

## Slide 4: Proposal (2)
In DC PC mode 1, the remaining power is allocated with the following priority order
  HARQ-ACK&SR > CSI > Data > SRS
    MCG > SCG for tie-breaks
    Decide between A-SRS = P-SRS and A-SRS > P-SRS
FFS between following two UE behaviors
  Alt.1: If the UE has only SRS transmission(s) in a CG, and the required power for the SRS is over the guaranteed power for the CG, and if the UE is power-limited, the SRS is dropped
  Alt.2: If the UE has only SRS transmission(s) in a CG, and the required power for the SRS is over the guaranteed power for the CG, and if the UE is power-limited, the SRS is power-scaled

## Slide 5: Proposal (3)
In DC PC mode 2, the remaining power is allocated based on the earlier transmission priority rule as in the case of PUCCH/PUSCH
  The earlier transmission is derived based on the subframe boundary and not based on the SRS starting timing