## Slide 1: Way forward on Evaluation Assumptions for Multiuser Superposition Transmission
NTT DOCOMO, MediaTek, LGE
3GPP TSG RAN WG1 Meeting #80bis
Belgrade, Serbia, April 20 – 24, 2015
Agenda Item: 7.2.7.2
R1-152229

## Slide 2: Proposals
For the evaluation of multiuser superposition transmission, the following cases are at least studied
  Transmissions to superposed UEs use the same transmission scheme
  FFS: mixed transmission scheme cases
The same precoder for the superposed UEs is considered.
  The case when rank1 precoder vector for UE1 is v1,1 and rank2 precoder matrix for UE2 is [v2,1 v2,2] and v1,1 = v2,1 is also considered as the same precoder case.
  Although this does not preclude different precoder case, companies should provide detailed assumption for different precoder case, e.g., availability of the other UE’s precoder information and receiver assumptions, etc.

## Slide 3: Proposals
SU-MIMO with MMSE-IRC receiver is considered as the baseline performance at least for 2x2 configuration.
  For inter-stream interference suppression, interference canceling receiver for SU-MIMO is also allowed, but companies should apply the same receiver for inter-stream interference suppression to MUST.

## Slide 4: Proposals
The following receiver studied in Rel-12 NAICS should be reused for superposed UE’s interference suppression as the starting point.
  For the CWIC,
    L2S mapping based on hard CWIC is used as the starting point.
    Assumptions including resource alignment between superposed UEs, detailed receiver assumptions and rate matching alignment between superposed UEs should be provided by companies.
    The other assumptions, e.g., HARQ, channel estimation, etc., should be provided by each company.
  For the symbol level IC such as R-ML,
    L2S mapping for multiuser superposition transmission should be further investigated.
    Resource alignment between superposed UEs is not necessarily assumed.
    The other assumptions, e.g., HARQ, channel estimation, etc., should be provided by each company.