## Slide 1: Clarification of DRS agreement from LAA ad-hoc
Huawei, Panasonic, [Alcatel-Lucent]
3GPP TSG RAN WG1 Meeting #80bis R1-152284
Belgrade, Serbia, 20th - 24th April 2015
Agenda item: 7.2.4.2
Document for decision

## Slide 2: Background: agreement (LAA ad-hoc)
DRS design should allow DRS transmission on an LAA SCell to be subject to LBT
Consider the following 2 options for the transmission of DRS within a DMTC window if LBT is applied to DRS
  Alt1: DRS is transmitted subjected to LBT in fixed subframe(s) within the configured DMTC
  Alt2: if LBT prevents transmission of DRS in the fixed subframe(s), allow the DRS to be transmitted in different subframe(s) within the configured DMTC if LBT succeeds
  Modifications to Rel-12 DMTC configuration are FFS
Note: this does not preclude the possibility to allow other DRS transmissions outside of the configured DMTC

## Slide 3: Background
The agreement covers FDD and TDD cases where the DRS can occupy one or multiple subframes
However, the agreement seems not preclude the possibility of transmitting DRS in different OFDM symbol positions within a subframe, for example if the structure of the DRS occasions was changed to a small number of consecutive OFDM symbols

## Slide 4: Proposed Clarification
DRS design should allow DRS transmission on an LAA SCell to be subject to LBT
Consider the following 2 options for the transmission of DRS within a DMTC window if LBT is applied to DRS
  Alt1: subject to LBT, DRS is transmitted in fixed time position within the configured DMTC
  Alt2: if LBT prevents transmission of DRS in the fixed time position, allow the DRS to be transmitted in different time positions within the configured DMTC if LBT succeeds
  Modifications to Rel-12 DMTC configuration are FFS
Note: this does not preclude the possibility to allow other DRS transmissions outside of the configured DMTC