## Slide 1: WF on initial downlink transmissions for LAA
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #80bis R1-152286
Belgrade, Serbia, 20th - 24th April 2015
Agenda item: 7.2.4.2
Document for decision

## Slide 2: Proposal 1
If LBT category 3 or 4 is adopted for LAA, the transmission of PDSCH can only start at predefined OFDM symbols
  At least 4 predefined symbols per subframe
  Transmission of PSS and SSS is tied to these predefined positions, for DRS and initial signal after successful CCA
  The transmission of CRS does not start earlier than PDSCH. CRS are transmitted at least in the same OFDM symbols as in Rel-8.

## Slide 3: Proposal 2
Right after a successful CCA check and before PDSCH, the initial signal transmissions from an LAA eNB consists of:
  First part: signal for channel reservation
    If needed until the start of the second part
  Second part: fractional OFDM symbol transmissions
    For channel reservation and for detection by other LAA eNBs
    One or more repetitions of a signal detectable by another eNB from the same or another operator. The duration of each repetition is shorter than one CCA slot
    UE does not need to receive these fractional OFDM symbol transmissions
  Third part: full OFDM symbol(s) transmission
    For detection by a served UE
      to identify the start of a serving eNB transmission
      for time and frequency synchronization (coarse and fine)
    Including at least one instance of PSS sequence and one instance of SSS sequence
    FFS: 1 or 2 full OFDM symbols
Right after a successful CCA check and before DRS, the initial signal transmissions from an LAA eNB consists of:
  Only the first part and the second part