## Slide 1: WF on UE-specific EPDCCH set initialization
NTT DOCOMO, NEC, Intel, KDDI, Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Sony
R1-152346
3GPP TSG RAN WG1 #80bis
Belgrade, Serbia, April, 20th-24th, 2015
Agenda item 7.2.1.1

## Slide 2: Background
Working assuming in RAN1 #80
  Rel-11 EPDCCH is a starting point for design of physical downlink control channel for MTC at least for MTC UEs in coverage enhancement.
In current specifications, UE-specific EPDCCH set is initialized via dedicated RRC signaling scheduled by PDCCH
For Rel.13 MTC UEs, the initialization of UE-specific EPDCCH set can’t be performed in traditional manner since Rel.13 MTC UEs are unable to detect the PDCCH

## Slide 3: Proposal 1
For Rel-13 MTC UEs in both normal coverage and enhanced coverage, the initialization of UE-specific EPDCCH configuration can be performed based on
  Alt.1: Dedicated RRC signaling scheduled by EPDCCH in common search space(CSS) if CSS is supported
    The parameters for UE-specific EPDCCH set initialization are included in the RRC signaling scheduled by EPDCCH in CSS
    FFS: The configuration and design of this CSS
  Alt.2: System information blocks for MTC
    The parameters for UE-specific EPDCCH set initialization are included in the SIBs
    FFS: Details of scheduling of SIB
  Alt.3A: Messages during RACH: RAR
    The parameters for UE-specific EPDCCH set initialization are included in the RAR
    FFS: Details of scheduling of RAR
    May be combined with Alt.1 or Alt.2
  Alt.3B: Messages during RACH: Message 4
    The parameters for UE-specific EPDCCH set initialization are included in message 4
    FFS: Details of scheduling of message 4