## Slide 1: WF on Transmission Mode Support of Rel-13 MTC UE
Qualcomm, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Ericsson, InterDigital, Verizon, ZTE
R1-154846
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.1.3

## Slide 2: Proposal
Reduced TM support for LC UEs and UEs operating CE
  Do not support TM5
  Do not support TM10
  Support TM1 and TM2 for CRS based demod
  Support DMRS-base TM
    Alt 1: TM9 with possible change of DCI, feedback
    Alt 2: Modified TM9 with per-RE precoding cycling as for distributed EPDCCH and possible change of DCI, feedback
  FFS: support of other TMs
  FFS: how to handle MBSFN subframes

## Slide 3: Appendix: Transmission Modes for PDSCH
TM | Purpose | Layer mapping for single layer operation
1 | Single antenna port, port 0 | Single antenna port
2 | Transmit diversity | SFBC / SFBC+FSTD
3 | Large delay CDD | SFBC / SFBC+FSTD
4 | Closed-loop spatial multiplexing | Rank 1 precoding
5 | Multi-user MIMO | Rank 1 precoding
6 | Closed-loop spatial multiplexing using a single transmission layer | Rank 1 precoding
7 | Single-antenna port, port 5; Rel.8 DMRS | Single antenna port / SFBC / SFBC+FSTD
8 | Dual layer transmission, port 7 and 8 or single-antenna port, port 7 or 8; Rel.9 DMRS | Single antenna port / SFBC / SFBC+FSTD
9 | Up to 8 layer transmission, ports 7-14 or single-antenna port, port 7 or 8; Rel.10 DMRS | Single antenna port / SFBC / SFBC+FSTD
10 | Up to 8 layer transmission, ports 7-14 or single-antenna port, port 7 or 8; Rel.10 DMRS + Rel.11 CSI enhancements | Single antenna port / SFBC / SFBC+FSTD