## Slide 1: Rank 2 codebook -- summary of RAN1 proposals and performance
Source: Samsung
3GPP TSG RAN WG1 Meeting #83 R1-156790
Anaheim, USA, 16th – 20th October 2015
Agenda item: 7.2.4.3.1
Title: Rank 2 codebook -- summary of RAN1 proposals and performance
Document for: Discussion and Decision

## Slide 2: High-Level Summary
Companies | Codebook size
Intel, ZTE, Huawei/HiSilicon, CMCC, Samsung/Ericsson/CATT/DOCOMO | 32
LGE | 34
ALU/ASB | 36
Qualcomm | 64 (34 CWs are used)
Companies | Config 3: Number of rank2 CWs complying nested property with rank 1 CWs
Samsung/Ericsson/CATT/DOCOMO Alt 2 | 3
Intel | 4
ZTE, Samsung/Ericsson/CATT/DOCOMO Alt 1 | 5
LGE, ALU/ASB, Qualcomm, Huawei/HiSilicon, CMCC | 8
Companies | Config 3: Number of 3D beams to construct rank1 & rank2 CWs codebook
LGE, ALU/ASB, Qualcomm, Huawei/HiSilicon, CMCC | 4
Samsung/Ericsson/CATT/DOCOMO Alt 2 | 6
ZTE, Samsung/Ericsson/CATT/DOCOMO Alt 1 | 7
Intel | 8

## Slide 3: Detailed Summary
Company | Comments
Intel | Same beam for both layers (orthogonality based on cross-pol) 4 beams; 2 co-phase values Orthogonal beam pair for two layers 2 orthogonal beam pairs in 1st dim; 2 orthogonal beam pairs in 2nd dim; 1 co-phase value Config 1-4 are not aligned with other companies
ZTE | Config 1 and Config 4 are aligned with most of the companies Config 3 is aligned with Samsung/Ericsson/CATT/DOCOMO Config 2 is different from other companies
LGE | Config 1 uses 8-PSK co-phase values Config 2-4 maintains nested property with rank 1 beams (legacy 8-Tx rank-2 beam pairs) – aligned with Qualcomm and ALU/ASB Config 2 is aligned with ALU/ASB Config 3 is aligned with Qualcomm Config 4 is aligned with most of the companies Codebook size = 34
Huawei/HiSilicon | Config 1-4 are not aligned with other companies Config 1 uses 8-PSK co-phase values (aligned with LGE) Config 4 uses (0,2) beam pair in place of (1,3), which is not a 8-Tx rank-2 beam pair Cophase values are Q-PSK with α parameter Maintains nested property with rank 1 beams (non-legacy 8-Tx rank-2 beam pairs)

## Slide 4: Detailed Summary
Company | Comments
Qualcomm | Config 2-4 maintains nested property with rank 1 beams (legacy 8-Tx rank-2 beam pairs) – aligned with LGE and ALU/ASB Config 3 is aligned with LGE Config 4 is aligned with most of the companies Codebook size = 64 (out of which 34 are used)
CMCC | Config 1-4 are not aligned with other companies Config 4 uses (0,2) beam pair in place of (0,3), which is not a 8-Tx rank-2 beam pair Maintains nested property with rank 1 beams (non-legacy 8-Tx rank-2 beam pairs)
ASB/ALU | Config 1: QPSK co-phase Config 2-4 maintains nested property with rank 1 beams (legacy 8-Tx rank-2 beam pairs) – aligned with LGE and Qualcomm Config 4 is aligned with most of the companies Codebook size = 36
Samsung/Ericsson/CATT/DOCOMO Alt 1 | Config 1 and Config 4 are aligned with most of the companies Config 3 is aligned with ZTE Config 2 is different from other companies
Samsung/Ericsson/CATT/DOCOMO Alt 2 | Config 1, Config 2, and Config 4 are aligned the same as Samsung/Ericsson/CATT/DOCOMO Alt 1 Alternate Config 3 is proposed

## Slide 5: Detailed Summary
Red beam pairs are non-legacy (non-8-Tx beam pairs)

## Slide 6: Discussion
Rank-2 codebook proposals are not quite aligned among different companies.
For codebook design, the following codebook design criterion can be considered:
  The master codebook size should be minimized, i.e., 32.
  Nested property between rank 1 and rank 2: To maintain UE complexity small, rank 1 & rank 2 codebook designs should be nested at least for some CWs or/and some Configs.
  Maintain Rel-10 8-Tx rank-2 beam pairs in the longer dimension: no strong motivation to deviate from that.
Observations:
  The proposals with the minimum master codebook size, i.e. 32, comprise Intel, ZTE, Huawei/HiSilicon, CMCC, Samsung/Ericsson/CATT/DOCOMO.
  The proposals complying nested property with rank 1 CWs comprise LGE, ALU/ASB, Qualcomm, Huawei/HiSilicon, CMCC.
  The proposals with the minimum number of 3D beams, i.e. 4, to construct rank1 & rank2 codebooks comprise LGE, ALU/ASB, Qualcomm, Huawei/HiSilicon, CMCC.

## Slide 7
Performance Comparison
SECD1 | Samsung/Ericsson/CATT/DOCOMO Alt1 (Config 3: checker-board)
SECD2 | Samsung/Ericsson/CATT/DOCOMO Alt 2 (Config 3: alternate proposal)
Z | ZTE
L | LGE
H | Huawei/HiSilicon
Q | Qualcomm
C | CMCC
A | ALU/ASB
I | Intel

## Slide 8: 16 port – Wide: SLS Results
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
3.1 | (4,2,2) | (8,8) | 70% | MU | UMa-200m
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
SECD1 | 22.47 | 18.52 | 5.51 | 100.00% | 100.00% | 100.00%
SECD2 | 22.47 | 18.79 | 5.67 | 100.02% | 101.46% | 102.87%
Z | 22.49 | 18.69 | 5.58 | 100.11% | 100.94% | 101.23%
L | 22.39 | 18.52 | 5.50 | 99.64% | 100.01% | 99.82%
H | 22.55 | 18.87 | 5.55 | 100.38% | 101.89% | 100.69%
Q | 22.42 | 18.73 | 5.47 | 99.79% | 101.16% | 99.38%
C | 22.52 | 18.69 | 5.52 | 100.23% | 100.94% | 100.22%
A | 22.43 | 18.69 | 5.54 | 99.81% | 100.94% | 100.51%
I | 22.70 | 19.14 | 5.57 | 101.04% | 103.35% | 101.05%
Chart: 
| 1 | 1.0145999999999999 | 1.0094000000000001 | 1.0001 | 1.0188999999999999 | 1.0116000000000001 | 1.0094000000000001 | 1.0094000000000001 | 1.0335000000000001
Y-Values | 1 | 1.0287 | 1.0123 | 0.9982 | 1.0069 | 0.9938 | 1.0022 | 1.0051 | 1.0105
50% UPT 
5% UPT 

## Slide 9: 16 port – Wide: SLS Results
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
SECD1 | 21.18 | 18.04 | 5.34 | 100.00% | 100.00% | 100.00%
SECD2 | 21.22 | 18.09 | 5.55 | 100.20% | 100.26% | 103.93%
Z | 21.20 | 17.94 | 5.63 | 100.09% | 99.41% | 105.45%
L | 21.16 | 17.86 | 5.48 | 99.90% | 98.97% | 102.68%
H | 21.28 | 18.00 | 5.66 | 100.49% | 99.78% | 106.03%
Q | 21.07 | 17.75 | 5.39 | 99.48% | 98.39% | 100.99%
C | 21.31 | 18.10 | 5.56 | 100.60% | 100.32% | 104.18%
A | 21.11 | 17.72 | 5.52 | 99.68% | 98.22% | 103.47%
I | 21.56 | 17.94 | 5.46 | 101.81% | 99.41% | 102.36%
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
3.3 | (4,2,2) | (8,8) | 70% | MU | UMi-2GHz
Chart: 
| 1 | 1.0025999999999999 | 0.99409999999999998 | 0.98970000000000002 | 0.99780000000000002 | 0.9839 | 1.0032000000000001 | 0.98219999999999996 | 0.99409999999999998
Y-Values | 1 | 1.0393 | 1.0545 | 1.0268 | 1.0603 | 1.0099 | 1.0418 | 1.0347 | 1.0236
50% UPT 
5% UPT 

## Slide 10: 16 port – Tall: SLS Results
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
3.1 | (2,4,2) | (8,8) | 70% | MU | UMa-200m
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
SECD1 | 17.52 | 13.96 | 3.70 | 100.00% | 100.00% | 100.00%
SECD2 | 17.42 | 13.96 | 3.76 | 99.46% | 100.04% | 101.54%
Z | 17.41 | 13.89 | 3.69 | 99.40% | 99.52% | 99.60%
L | 17.27 | 13.61 | 3.64 | 98.59% | 97.48% | 98.35%
H | 17.44 | 13.77 | 3.71 | 99.52% | 98.70% | 100.24%
Q | 17.33 | 13.79 | 3.72 | 98.92% | 98.83% | 100.30%
C | 17.31 | 13.94 | 3.60 | 98.81% | 99.86% | 97.19%
A | 17.42 | 13.84 | 3.74 | 99.43% | 99.18% | 101.03%
I | 17.67 | 14.13 | 3.79 | 100.88% | 101.28% | 102.29%
Chart: 
| 1 | 1.0004 | 0.99519999999999997 | 0.9748 | 0.98699999999999999 | 0.98829999999999996 | 0.99860000000000004 | 0.99180000000000001 | 1.0127999999999999
Y-Values | 1 | 1.0154 | 0.996 | 0.9835 | 1.0024 | 1.003 | 0.9719 | 1.0103 | 1.0229
50% UPT 
5% UPT 

## Slide 11: 16 port – Tall: SLS Results
Proposals | Avg UPT | 50% UPT | 5% UPT | Avg UPT gain | 50% UPT gain | 5% UPT gain
SECD1 | 16.39 | 13.03 | 3.63 | 100.00% | 100.00% | 100.00%
SECD2 | 16.58 | 13.29 | 3.72 | 101.18% | 102.00% | 102.56%
Z | 16.24 | 12.90 | 3.56 | 99.12% | 99.03% | 98.10%
L | 16.39 | 13.07 | 3.61 | 100.01% | 100.33% | 99.59%
H | 16.35 | 13.06 | 3.60 | 99.77% | 100.21% | 99.31%
Q | 16.43 | 13.07 | 3.64 | 100.27% | 100.33% | 100.44%
C | 16.36 | 12.84 | 3.61 | 99.85% | 98.54% | 99.48%
A | 16.37 | 12.86 | 3.62 | 99.90% | 98.72% | 99.92%
I | 16.79 | 13.42 | 3.74 | 102.47% | 103.02% | 103.17%
Lambda | (N1,N2,P) | (O1,O2) | Target RU | Mode | Channel
3.3 | (2,4,2) | (8,8) | 70% | MU | UMi-2GHz
Chart: 
| 1 | 1.02 | 0.99029999999999996 | 1.0033000000000001 | 1.0021 | 1.0033000000000001 | 0.98540000000000005 | 0.98719999999999997 | 1.0302
Y-Values | 1 | 1.0256 | 0.981 | 0.9959 | 0.9931 | 1.0044 | 0.9948 | 0.9992 | 1.0317
50% UPT 
5% UPT 

## Slide 12: Conclusion
Based on simulation results, we can observe that
  Performance of different rank 2 codebook proposals vary depending on channel models and antenna port layouts.
  However, the performance difference across different proposals is marginal.
Proposal: Adopt a rank 2 codebook proposal in R1-156381 as Rel-13 class A rank-2 codebook.