## Slide 1: WF on time and frequency relationships for MTC
Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Nokia Networks, Sequans, Intel, LG Electronics, CATT, Qualcomm, Sierra Wireless, Samsung, Panasonic, MediaTek, InterDigital, ZTE, Verizon Wireless
R1-157473
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.2

## Slide 2: Proposal for UL repetition postponing
RAN1#82bis agreement:
  A UE will postpone transmitting PUSCH/PUCCH repetition (when R > 1) to the next available UL subframe in invalid UL subframe indicated by MTC-SIBx.
    In case of PUSCH/PUCCH with R = 1, a UL grant or PDSCH transmission overrides the MTC-SIBx configuration, thus a UE will transmit PUSCH/PUCCH
Agree that the expression ‘PUSCH/PUCCH repetition’ in the above agreement also concerns the first subframe (when it is followed by repetitions).

## Slide 3: Proposal on timing relationships
When PUSCH is scheduled by M-PDCCH where the M-PDCCH transmission ends in subframe n then PUSCH starts in subframe n+4 assuming that n+4 is a valid UL subframe.
When PDSCH is scheduled by M-PDCCH, the timing relationship between the end of the PDSCH transmission and the beginning of the PUCCH transmission carrying HARQ-ACK follows the legacy timing relationship between PDSCH and PUCCH assuming that this results in PUCCH being transmitted in a valid UL subframe.

## Slide 4: Proposal for UL retuning gaps
Cases for UL retuning to consider:
  Case 1: UE retunes from PUSCH narrowband to PUSCH narrowband
  Case 2: UE retunes from PUCCH narrowband to PUCCH narrowband
  Case 3: UE retunes from PUCCH narrowband to PUSCH narrowband
  Case 4: UE retunes from PUSCH narrowband to PUCCH narrowband
  Case 5: UE retunes from PRACH narrowband to PRACH narrowband
Options for how to define the UL retuning gap:
  Option A: Last two symbols of the earlier subframe
  Option B: Last symbol of the earlier subframe + first symbol of the later subframe
  Option C: Guard subframe (not needed according to results in R1-157472)
  Option D: First two symbols of the later subframe
Agree on the following:
  Case 1: Option B
  Case 2: Option B
  Case 3: Option D
  Case 4: Option A (working assumption)
  Case 5: FFS

## Slide 5: Proposal for PRS collision
When M-PDCCH/PDSCH transmission collies with PRS transmission in a subframe,
  LC/CE UE is not required to know the PRS configuration.
  It is up to eNB whether to drop or puncture transmissions.

## Slide 6: Proposal for valid DL subframes
When valid DL subframes are indicated with a bitmap in SIB1bis, the bitmap length is 10 or 40 bits.