## Slide 1: Way Forward on NB-IoT
CMCC, Vodafone, Ericsson, Huawei, Hisillicon, Deutsche Telekom, Mediatek, Qualcomm, Nokia Networks, Samsung, Intel, Nuel, CATR, AT&T, NTT DOCOMO, ZTE, Telecom Italia, IITH, CEWiT, Reliance-Jio, CATT, u-blox, China Unicom, LG Electronics, , Panasonic, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, China Telecom
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22th November 2015
R1-157783

## Slide 2: Proposal on NB-IoT uplink
Single-tone transmissions are supported
  2 numerologies should be configurable for Single-tone transmission: [3.75]kHz and 15kHz
  A cyclic prefix is inserted
  Frequency domain Sinc pulse shaping in the physical layer description
Multi-tone transmissions are supported
  Multi-tone transmissions are based on SC-FDMA
  15 kHz UL subcarrier spacing
  Additional mechanisms for PAPR reduction FFS
The UE shall indicate the support of Single-tone and/or Multi-tone
  Details to be discussed by WGs

## Slide 3: Proposal on NB-IoT Downlink
Downlink transmission with 15kHz subcarrier spacing for all the scenarios: standalone, guardband, in-band