## Slide 1: WF on Paging
Nokia Networks
R1-157827
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.3

## Slide 2: Background
Agreements from RAN1#82bis –
  Confirm the working assumption to use M-PDCCH scheduled PDSCH carrying paging record(s)
  One or more narrowbands can be configured by eNB for paging
    A UE monitors a paging occasion in one of the configured narrowbands in the subframe based on at least UE ID at least for paging record(s)

## Slide 3: Proposal
How to indicate set of M-PDCCH narrowband(s) for paging
  Option 1: implicit mapping
    Option 1A: 1st narrowband = PCID mod N_NB_paging
    Option 1B: 1st narrowband = 0
    Other narrowbands are in consecutive order from 1st narrowband with wrap-around
  Option 2: via MTC-SIB
    Bitmap (up to 16 bits)

## Slide 4: Proposal
When more than one narrowband is configured for M-PDCCH for paging
  The narrowband is selected based on UE ID
    Option 1: N_ind = UE ID mod N_NB_paging
    Option 2: N_ind = ((UE ID*A) mod D) mod N_NB_paging
        A = 39827 and D = 65537