## Slide 1: WF on Remaining Issues on Number of Repetitions
Sony, [CATT]
R1-157872
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.4

## Slide 2: Background on repetitions
Agreement
Set of PDSCH/PUSCH Repetition Numbers
The predefined set of PDSCH/PUSCH repetition numbers are: {1, 2, 4, 8, 16, 32, 64, 128, [192], 256, [384], 512, [768], 1024, [1536], [2048]}
“Set of PDSCH repetition numbers” and “Set of PUSCH repetition numbers” are derived based on each respective 4-bit indicator signalled in MTC-SIB:
    Mode A: 4 values
    Mode B: 8 values
    Default values:
      Mode A: set = {1,2,4,8}
      Mode B: set = {4,8,16,32,64,128,256,512}
FFS whether or not there is a restriction on the max number repetitions for Mode A

## Slide 3: Proposal on repetitions for Mode A
  Alt 1: For Mode A, the 4-bit indicator provides an index to a table
    A single table is used that is common to the UL and DL
index | Set of repetitions
0 (= default) | 1,2,4,8
1 | 1,4,8,16
2 | 1,2,4,16
3 | 1,4,16,64
others | reserved
  Note: FFS on max number of repetitions for mode A is resolved by this table: max = 64
  Alt.2:
    Only the default values of {1,2,4,8} apply in Mode A. No signalling is necessary

## Slide 4: Proposal on repetitions for Mode B
  Alt1: For Mode B, the 4-bit indicator provides an index to a table
    A single table is used that is common to the UL and DL
index | Set of repetitions | motivation
0 | 4,8,16,32,64,128,256,512 | Motivated by mode A, index 0
1 | 8,16,32,64,128,256,512,1024 | Motivated by mode A, index 1,2
2 | 8,32,128,192,256,384,512,768 | Better granularity at high R
3 | 4,16,64,256,384,512,768,1024 | Good granularity at high R, overlap at low R
4 | 4,16,64,256,512,1024,1536,2048 | Large UL TrBlks
5 | 1,2,4,8,16,32,64,128 | ModeB-only network
6 | 1,4,16,64,256,512,1024,2048 | ModeB-only network, large TBS
7 | 1,4,16,32,64,128,256,512 | ModeB-only network, coverage
Others | reserved | 
  Alt 2:
    Indicator is an index from the start of the predefined set
    “Set of PxSCH repetition numbers” are 8 consecutive values starting from offset

## Slide 5: Proposal on Predefined Set
Proposal:
The predefined set of PDSCH/PUSCH repetition numbers is: {1, 2, 4, 8, 16, 32, 64, 128, 192, 256, 384, 512, 768, 1024, 1536, 2048}