## Slide 1: WF on UCI remaining issues
LG Electronics, Ericsson, Panasonic, ...
R1-163440
3GPP TSG RAN WG1 #84bis
Busan, Korea, April 11 - 15, 2016
Agenda 7.2.1.2.3

## Slide 2: Proposals
  For frequency resource of A/N transmission
    The number of DCI bits for frequency offset is 2 bits with 15 kHz and 3 bits with 3.75 kHz
    The subcarrier for A/N transmission is f= f0 + delta_f
    For 15 kHz
      The reference subcarrier index (f0) for A/N transmission is fixed as ‘0’ in the specification
      Offset values (delta_f) are {0, 1, 2, 3}
    For 3.75 kHz
      The reference subcarrier index (f0) with 3.75 kHz A/N transmission is fixed as ‘45’ (i.e., the 3rd subcarrier from the last in a PRB) in the specification
      Offset values (delta_f) are {0, -1, -2, -3, -4, -5, -6, -7}

## Slide 3: Proposals
  Time offset (i) of A/N resource is indicated in DL grant
    The number of DCI bits for time offset is 2 bits for 15 kHz and 1 bit for 3.75 kHz
    i = 0, 1, 2, 3 for 15 kHz, i = 0, 1 for 3.75 kHz
    The gap value, K (i) = i * A/N resource unit duration in time
  A UE transmits A/N at starting subframe n + 12 + K (i) where subframe n is the end of the corresponding PDSCH transmission