## Slide 1: WF on Further Details of DL Gap Configuration for NB-IoT
Ericsson, Intel, …
R1-163448
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th -15th April 2016
Agenda item 7.2.1.1.1

## Slide 2: Background (1)
Working Assumption:
At least for UEs in extreme coverage (FFS how the UE knows its coverage level for the purpose of knowing which gap configuration applies, if any), for transmission in downlink which requires large number of repetitions, DL gaps can be introduced during the repetitions of NPDSCH and NPDCCH
  Note: During a DL gap, UEs other than those configured with the particular gap can receive their NPDSCH and/or NPDCCH
  Gap configuration is provided by SIB signaling
    Configuration information is composed of a subset of the following:
      Gap enable/disable, Gap starting point (periodicity, offset), Gap size, number of Gaps for Rmax repetitions
      Exact subset is FFS.
    FFS how many gap configurations are needed
For a given UE, the subframes designated as DL gap are treated as invalid DL subframes for the given UE
  Invalid subframe means: When overlapping with a DL gap, PDCCH and PDSCH repetitions are FFS (until RAN1#84bis)
    either postponed to the next valid DL subframe
    or skipped
Note that these gaps do not apply in Idle Mode.
Note that this does not impact downlink-uplink timing relationships
Email agreement until Thursday 31st March to close FFS points in the first main bullet. When all RRC details are agreed for these gaps, working assumption for the first main bullet will automatically be confirmed.

## Slide 3: Background (2)
RAN1 post NB-IoT adhoc#2 email agreements:
“FFS how the UE knows its coverage level for the purpose of knowing which gap configuration applies, if any”
  For RACH Msg2 and Msg4, the UE knows its gap configuration according to R_NPDCCH_max configuration of the CSS for Msg2 (i.e., RAR) transmission. This is also the default gap configuration for DL transmission after Msg4.
  For DL transmissions after Msg4, the UE knows its gap configuration according to the UE-specific R_NPDCCH_max configuration. In case there is no R_NPDCCH_max configuration, the UE uses the default gap configuration.
“Exact subset is FFS”
  The subset is: {Gap starting point periodicity, Gap size}.
  Gap configuration provides indication on if the DL transmission gap is enabled or disabled.
  Gap starting point is defined over absolute subframe number.
“FFS how many gap configurations are needed”
  At least one threshold X1 is defined, and correspondingly one gap configuration can be signaled for R_NPDCCH_max >= X1;
  Decide till RAN1#84bis if a second threshold X2 is defined, and correspondingly a second gap configuration can be signaled for X1 > R_NPDCCH_max >= X2.

## Slide 4: Proposal (1)
Starting point of gap periods is (SFN=0, sf=0)
Gap starting point periodicity is defined based on cell-specific valid DL subframes for NPDCCH/NPDSCH transmission
Gap size is defined based on cell-specific valid DL subframe for NPDCCH/NPDSCH transmission

## Slide 5: Proposal (2)
{Gap starting point periodicity, Gap size} is signaled jointly
For UEs with R_NPDCCH_max >= X1, {Gap starting point periodicity, Gap size} is configured with 2 bits indicating the following:
  {X1, X1/2};
    i.e., X1/2 subframes for transmission per period
  {X1* 3/4, X1/4};
    i.e., X1/2 subframes for transmission per period
  {X1/2, X1/4};
    i.e., X1/4 subframes for transmission per period
  {X1/4, X1/8};
    i.e., X1/8 subframes for transmission per period

## Slide 6: Proposal (3)
A cell-specific value of X1 is signaled in SIB1
  2 bits are used to indicate X1 from {32, 64, 128, 256}