## Slide 1: WF on DMRS-based Open-Loop and Semi-Open-Loop MIMO
CATT, Alcatel-Lucent Shanghai Bell, CATR,
Intel, Huawei, HiSilicon, Nokia, Samsung
3GPP TSG RAN WG1 Meeting #84bis R1-163455
Busan, S. Korea, April 11- 15, 2016
Agenda item: 7.3.3.3

## Slide 2: Proposal
Evaluate open-loop and semi-open-loop MIMO schemes until RAN1#85
  Summary of schemes proposed in RAN1#84b is provided in the following slides
  NOTE: other schemes are not precluded
Performance, CSI feedback and transmission details should be provided

## Slide 3: Example: a CSI-process with K = 1 CSI-RS
Alt-1a: Transparent DMRS (i.e. DMRS and PDSCH precoded identically)
  PMI feedback points to one of N precoding hypotheses, where each precoding hypothesis corresponds to a set of M>1 precoding matrices on a subband
    PMI overhead log2(N) bits, where N can be 1
  Example:
    PRB-level or subcarrier-level cycling of M precoders
    Cycling for a subset of codebook by Codebook-subset-restriction
    Cycling for i2, not for i1 (W1 reporting only for dual-stage codebook, e.g. Rel.10 8Tx, Rel.12 4Tx, Rel.13 Class A and its possible Rel.14 enhancements)
Alt-1b: Non-transparent DMRS (i.e. DMRS and PDSCH precoded differently)
  Received PDSCH signal as y = HW1W2s + n, where, S is unprecoded PDSCH, W2 refers to OL-precoding from L layer PDSCH to D DMRS ports, W1 refers to CL-precoding from DMRS/PDSCH to CSI-RS ports
  RI/PMI feedback: quantization of W1, based on H and knowledge of W2
  CQI feedback: quantization of HW1W2
  Example of W2 precoding (open-loop)
    Rank-1: SFBC (RE-level)
    Rank-2: LD-CDD

## Slide 4: Example: a Class B CSI-process with K>1 CSI-RS
Alt-2a:
  A single wideband CRI report
  Open-loop/semi-open-loop with K=1 is performed in the CSI-RS resource indicated by CRI
Alt-2b:
  CRI cycling, no CRI report
  open-loop/semi-open-loop with K=1 is performed in the corresponding CSI-RS resource indicated by CRI