## Slide 1: WF on spatial consistency
Intel, InterDigital, Huawei, HiSilicon
R1-163467
3GPP TSG RAN1 #84b
Busan, Korea, April 11 - 15, 2016
Agenda Item: 8.2.3.2

## Slide 2: Background
In RAN1 ad hoc on Channel modeling, spatially consistent random number based approach (R1-161726) is agreed as working assumption for spatial consistency modeling
  The working assumption is sufficient for drop based MU-MIMO simulation
  However, it was observed by R1-162244, R1-162389 that the delay/angle may vary faster than physically allowed along a UE trajectory and this could impact the beam mobility simulation

## Slide 3: Proposal
Confirm the working assumption of R1-161726 as agreement for drop based MU-MIMO simulations
  The correlation distance for cluster-specific random variables is 50m for UMa, 15m for UMi and 10m for indoor
  The correlation distance for LoS state is 50m for UMa and 15m for UMi

## Slide 4: Proposal
For beam mobility simulations when UE position needs to be updated:
  When UE is dropped into the network, e.g. at t0=0, use R1-161726 to generate channel cluster power/delay/angles
  Update channel cluster power/delay/angles at t0+t based on UE channel cluster power/delay/angles, moving speed and direction at t0
    Cluster power at is generated using step 6 with cluster delay
    =v(,0)
    v is UE moving speed in the horizontal plane
    is UE moving direction in the horizontal plane
    is 2D distance between Tx/Rx; is 3D distance between Tx/Rx
    and are cluster specific reflection surface angles; for LoS path, set to 0; for NLoS clusters, generate using spatially consistent random numbers with uniform distribution U(-180, 180) with 50m correlation distance

## Slide 5: Proposal
Define soft LoS state to smooth channel if UE moves between different channel states
  Soft LoS state is a float number between 0 (NLoS) and 1 (LoS)
  Soft LoS state generating method is according to the appendix
    dLoS is FFS
Define path loss and channel matrix to be a function of soft LoS state
UE is not allowed to move between indoor/outdoor states

## Slide 6: Appendix: generating soft LOS/NLOS
A spatially consistent Gaussian number G with autocorrelation distance dLOS (e.g. 50m) is generated. This is combined with a threshold value F determined via
  Here is the distance and is the LOS probability function. The soft LOS state is determined by a function approximating knife-edge diffraction: