## Slide 1: WF on Dynamic Blockage
Qualcomm, Intel, [Interdigital], Samsung, Nokia, Shanghai Bell, E/// …
R1-163473
3GPP TSG RAN1 #84B
Busan, Korea, Apr11 - 15, 2016
Agenda Item: 8.2.3.1

## Slide 2: Background
In R1-161150, below working assumption is agreed:
  The blockage caused by the static objects and moving objects such as human body and vehicle: The blockage attenuation generally increases with frequency
Further, in R1-161142 the following underlined agreements are also relevant towards the blockage modeling
  Complexity in terms of Description, Generating channel coefficients, development complexity and Simulation time should be considered.
  The model should be consistent in space, time and frequency
Further, based on the agreed WF proposal R1-161739, we have the following additional details.

## Slide 3: WF Proposal
Propose a stochastic model for human and vehicle blocking:
Proposal 1: The blockers are modeled as (multiple) an angular blocking region as applied to the AoA/ZoA around the UE.
  Blockage modeling is an optional feature – it can be turned on in InH, UMi or UMa scenario to consider the effect of human or vehicular blockage
Proposal 2: One of the angular blocking regions represents self-blocking (i.e. human/hand holding the UE); this blocking region is not spatially consistent and UE specifically generated.
  This is an optional step
Proposal 3: The angles and sizes of the angular blocking region (non self blocking) are generated on a per UE basis according to a statistical process
  The center of the blocking region is uniformly chosen in the azimuth angle. Fixed in elevation, elevation = 90*;
  A3: Size of the blocking region is x deg in azimuth and y deg in elevation, where x and y are constants, provided in following table
  B3: Size of blocking region is generated by simulating an imaginary screen placed at a random distance from UE

## Slide 4: WF Proposal
Proposal 4: On number of angularly blocked regions (excluding self-blocking)
  The total number of angularly blocked regions K = 5. (1 self blocking and K -1 other blocking)
  FFS: The dependence on the number of angular blocked regions as a function of user density
Proposal
  A5:
    The clusters within the angular blocking regions are attenuated assuming a statistical model; Shadowing is chosen from a statistical distribution F(.) - lognormal shadowing
  B5:
    Attenuation is based on knife edge model
Table for above proposals – Values in square brackets
 | xk | φk | yk | θk | Loss (in dB) InH | Loss in dB UMI | Loss in dB UMa
k = 1 (Portrait) | 120o | 260o | 80o | 100o | 30 | 30 | 30
k = 1 (Landscape) | 160o | 40o | 75o | 110o | 30 | 30 | 30
k = 2, …, 5 | 2.5o | Unif([0, 2π]) | 15o | π/2 | LnN(15 dB,σ2 = 3) | Ln N(8 dB,σ2 = 3) | Ln N(4dB,σ2 = 3)

## Slide 5: WF Proposal
Proposal 6: The blocking model is made spatially consistent.
  A6: The blocking parameters are generated using the same methods utilized for spatial consistency in the TR
  B6: The blockage screens are physically placed on the map (map based) to generate spatially consistent blocking
Proposal 7: The blocking model is made temporally consistent
  A7: To model the mobility of the blockage, one can consider the following approach
  B7: To model the mobility, the blockers are moved in the coordinate system (map based)
Angular Blockage
2D = cluster width
d
d=angular distance from cluster center to edge of blockage
Attenuation
d = angular distance
0
D
Attenuation chosen in proposal A5
Example equation

## Slide 6: WF Proposal
Proposal A8: Use the following flow for channel generation
Note:
  The blockage does not change LOS/NLOS state of a link.
  Note: Temporal variability is on-demand, Blockage modeling is add-on feature.

## Slide 7: WF
Down-select between either A or B options for proposal 3,5,6 and 7.