## Slide 1: [DRAFT] WF on power control of uplink ACKNAK
Huawei, HiSilicon, Samsung, Ericsson, …
R1-16xxxx
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.2.1.2.5

## Slide 2: Background
Agreements:
  For NB-PUSCH data transmission, the uplink power setting re-use section 5.1.1.1 of 36.213, that is for serving cell c and subframe i ( for 15 kHz subcarrier spacing) or NB-Slot i (for 3.75 kHz subcarrier spacing)
    PNPUSCH,c(i)=min{PCMAX,c(i), 10log10(MNPUSCH,c(i))+PO_NPUSCH,c+ αc(j) PLc+fc(i)}
    …
  UL power control for ACK/NACK transmission uses the same procedure as normal NB-PUSCH transmission.
    Alt. 1: Accept above formulas
    Alt. 2: With alpha = 1
Since the reliability of ACK/NACK transmission has been considered in UCI design, different power controlis not needed, which would disturb UE power setting.

## Slide 3: Proposals
    Adopt Alt 1 for uplink ACK/NACK transmission
  Uplink power setting of ACK/NACK corresponding to NB-PDSCH transmission is the same as NB-PUSCH data transmission.