## Slide 1: [DRAFT] WF on Power Headroom Report
Huawei, HiSilicon,…
R1-16xxxx
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.2.1.2.5

## Slide 2: Background
Agreement:
  RAN1 recommends to support transmission of NB-PHR with Msg3 of random access procedure using 2 bits for the lowest configured NB-PRACH repetition level, subject to RAN2 confirmation of available bits
    Dynamic indication utilizing DCI is not supported
    Note: Above does not request to change Msg. 3 size
  The number of subcarriers supported in NPUSCH transmission is {1, 3, 6, 12}.
PHR is used by eNB to determine how much uplink bandwidth UE can use before exceeding maximum transmit power.
UE can indicates to eNB its supported maximum number of subcarriers instead of coarse power headroom
  With coarse power headroom, eNB is very likely to have erroneous estimation on the maximum number of subbcarriers UE can support.

## Slide 3: Proposals
In NB-PHR, the UE indicates the maximum number of subcarriers it can transmit on before exceeding its maximum transmit power, i.e. one of {1, 3, 6, 12}.
Use of NB-PHR bits for single-tone UEs is up to RAN2