## Slide 1: [DRAFT] WF on bandwidth component of uplink power control
Huawei, HiSilicon, Samsung, Sharp, Ericsson, …
R1-16xxxx
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.2.1.2.5

## Slide 2: Background
Agreements:
  For NB-PUSCH data transmission, the uplink power setting re-use section 5.1.1.1 of 36.213, that is for serving cell c and subframe i ( for 15 kHz subcarrier spacing) or NB-Slot i (for 3.75 kHz subcarrier spacing)
    PNPUSCH,c(i)=min{PCMAX,c(i), 10log10(MNPUSCH,c(i))+PO_NPUSCH,c+ αc(j) PLc+fc(i)}
    MNPUSCH,c(i)
      Alt 1: {1/4, 1,3,6,12} (reflecting UL transmission resource BW)
      Alt 2: {1,3,6,12} (3.75 kHz is adjusted by using PO_NPUSCH,c)
    …
In LTE, the assigned uplink bandwidth is reflected by MNPUSCH,c(i) in uplink power control.
Adjusting PO_NPUSCH,c introduces further standardization and implementation complexity.

## Slide 3: Proposals
    Adopt Alt 1 for MNPUSCH,c(i), i.e. MNPUSCH,c(i) is one of {1/4,1,3,6,12} where 1, 3, 6, 12 are for 15 kHz subcarrier spacing and 1/4 is for 3.75 kHz subcarrier spacing.