## Slide 1: [DRAFT] WF on fc(i) in uplink power control
Huawei, HiSilicon, Samsung, Intel…
R1-16xxxx
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.2.1.2.5

## Slide 2: Background
Agreements:
  For NB-PUSCH data transmission, the uplink power setting re-use section 5.1.1.1 of 36.213, that is for serving cell c and subframe i ( for 15 kHz subcarrier spacing) or NB-Slot i (for 3.75 kHz subcarrier spacing)
    PNPUSCH,c(i)=min{PCMAX,c(i), 10log10(MNPUSCH,c(i))+PO_NPUSCH,c+ αc(j) PLc+fc(i)}
    …
    fc(i)
      Alt 1: A power adjustment parameter indicated by DCI
      Alt 2: No TPC command, fc(i)=0
    …

## Slide 3: Background
The infrequent, short duration characteristics of typical Cellular IoT traffic means that the closed-loop power command may be outdated because the targeted uplink data transmission has already ended prior to the reception of the power command;
Tight timeline may not be maintained for the scheduling and uplink transmissions in the NB-IoT system so a power adjustment signal may not be available on demand;
Frequent air-interface interactions for the measurement report and power adjustment will bring significant over-the-air overheads and therefore will cause degraded network capacity and increased UE power consumption.
The work of close loop power control can be taken by scheduling flexibilities, such as repetition, TBS and MCS etc.
With TPC, the DCI performance is degraded due to more bits.

## Slide 4: Proposals
    Adopt Alt 2 for fc(i) in uplink power control, i.e. no TPC command, fc(i)=0.