## Slide 1
3GPP TSG RAN WG1 Meeting #84bis R1-163549
Busan, Korea, 11th - 15th April 2016
Agenda item: 7.3.3.1.1
WF on additional REs for Class A NZP CSI-RS resource
Intel

## Slide 2: Motivation
Support of Class A CSI-RS with 32 antenna ports using the legacy CSI-RS REs would limit the maximum reuse of CSI-RS to 5 in FDD systems
Reducing the density for Class A CSI-RS resource may not be feasible due to Rel-10 design assumptions for non precoded CSI-RS
To increase the CSI-RS reuse the additional REs should be released in the downlink subframe for Rel-14 NZP CSI-RS resources

## Slide 3: Proposal
Rel-14 NZP CSI-RS resource is transmitted using REs of at least Rel-10 CSI-RS configurations
FFS: Additional REs for Rel-14 NZP CSI-RS resource assuming “CRS-less” downlink subframes