## Slide 1: WF on CSI measurement with respect to R_CSI, max
Panasonic, Qualcomm
R1-163552
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11-15 April, 2016
Agenda item 7.1.5

## Slide 2: Background
For narrowband CSI
  RCSIMax <= Ych
    With single narrowband of "last subframes of the period of nCQI_ref", UE cannot report the best narrow band as only one narrowband is measured.
  RCSIMax > Ych
    What is the definition of narrowband CSI measurement?
For wideband CSI
  RCSIMax < Ych x (number of hopping frequencies)
    What is the definition of wideband CSI measurement?
  RCSIMax mod (Ych) is not zero
    The number of subframes are not equal among narrowbands
Note that Ych is the subframe period of the same frequency in the frequency hopping.

## Slide 3: Proposal for the working assumption
For narrowband CSI
  RCSIMax <= Ych
    the reference subframes are defined as the last subframes of the period of nCQI_ref for each hopping narrowband.
  RCSIMax > Ych
    The time location of the reference subframes is not defined but UE should reflect the situation of the last subframes of Ych for each hopping narrowband.
    The period of the reference subframes should take into account as the offset of CQI value i.e. if RCSIMax = 2 ms, it means spectral efficiency is scaled by a factor of 2.
For wideband CSI
  RCSIMax < Ych x (number of hopping frequencies) and/or RCSIMax mod (Ych) is not zero
    The time location of the reference subframes is not defined but UE should reflect the situation of the last subframes of Ych x (number of hopping frequencies).
    The period of the reference subframes should take into account as the offset of CQI value i.e. if RCSIMax = 2 ms, it means spectral efficiency is scaled by a factor of 2.