## Slide 1: WF on Scheduling Collision
Sony, Intel, MediaTek, Sequence
R1-163553
3GPP TSG RAN WG1 84bis
Busan, Korea 11th - 15th April 2016
Agenda item 7.2.1.1.1

## Slide 2: Background (1)
After NB-PDCCH 1 schedules a data channel, if another NB-PDCCH 2 schedules another data channel between NB-PDCCH 1 and the corresponding data channel a collision can occur.

## Slide 3: Background (2)
After an NB-PDSCH, if an uplink grant for a NB-PUSCH carrying data is scheduled between the end of the NB-PDSCH and the corresponding acknowledgement, a collision between the acknowledgement and the NB-PUSCH carrying data may occur

## Slide 4: Proposal
An NB-IoT UE that has received a grant from an NB-PDCCH is not required to monitor NB-PDCCH for any further DL or UL grant during the time period between the end of the NB-PDCCH that schedules the grant and the start of the corresponding NB-PDSCH or NB-PUSCH transmission
An NB-IoT UE is not required to monitor for an NB-PDCCH for any further DL or UL grant during the time period between the start of a NB-PDSCH transmission and the start of the NB-PUSCH transmission carrying the ACK/NACK
An NB-IoT UE is not required to monitor for a NB-PDCCH search space within 1 ms after the end of the NB-PUSCH transmission
  UE shall monitor for NB-PDCCH search space for DL grant between the period 1ms after the end of NB-PUSCH transmission and the potential start of an UL grant acknowledging that NB-PUSCH transmission