## Slide 1: Way forward on evaluation assumptions for 5G waveform
Huawei, HiSilicon, [NTT DOCOMO], [Nokia], [Intel], [MediaTek], [Samsung], [LGE], [Ericsson], [QualComm]
3GPP TSG RAN WG1 Meeting #84bis R1-163556
Busan, Korea, 11th – 15th April 2016
Agenda Item: 8.1.3

## Slide 2: Background
NR should have,
forward compatibility
multiple numerologies for many reasons, e.g. wide spectrum ranges, large bandwidth, diverse deployments and services, etc..
Waveform design is a fundamental component that needs to address the above issues, and appropriate evaluation should be defined
Evaluation method
Evaluation cases
Evaluation metrics
Evaluation parameters

## Slide 3: Proposal (Evaluation method)
Link level simulation is used for waveform evaluation.
  Whether and how to do system level simulation for waveform is FFS.

## Slide 4: Proposal (Evaluation cases)
Four evaluation cases should be used in link level simulation, which are
  Case 1: DL single numerology case
  Case 2: DL mixed numerology case
  Case 3: UL single numerology case (asynchronous transmission)
  Case 4: UL mixed numerology case (synchronous transmission)
(refer to their illustrations on next pages)

## Slide 5: Proposal (Case 1)
(a) Downlink single numerology case
Gsys
Gsys
BWcarrier
Spectrum mask
Signal transmission bandwidth
Numerology 1
2
2
(System guard band)

## Slide 6: Proposal (Case 2)
(b) Downlink mixed numerology case
Gsubband
Numerology 1
2
Numerology 2
(Inter-subband guard band)
The target user is at the edge of the “target” subband.
Interfering subband
Target UE
Notes: Evaluation should be taken under [0~5] subcarriers for guard tones between sub-bands (i.e., inter-subband guard band, see above figure)

## Slide 7: Proposal (Case 3)
(c) Uplink single numerology case (asynchronous transmission)
(Inter-user guard band)
Receiver
Notes: BW takes into account the guard overheads
Same power offset for both UE2 and UE3?
Bandwidths of UE2 and UE3 have impact on the results/interferences
Evaluation should be taken under [0~5] subcarriers of guard tones between UEs (i.e., inter-UE guard band, see above figure).

## Slide 8: Proposal (Case 4)
(d) Uplink mixed numerology case (synchronous transmission)
Note: Only the target UE is evaluated while the other two UEs are interferers. The value of power offset is discussed in the table of detailed simulation assumptions.

## Slide 9: Proposal (Evaluation metrics)
User spectrum efficiency as performance metric
  Take into account guard band and time domain overhead. The values and their calculation method of guard band and time domain overhead should be reported.
  BLER vs SNR should be reported for calibration
  OOBE level is reported
PAPR/Cubic metric
EVM
Rx processing delay
Complexity (FFS: how to quantify)
The following is also reported
  Receiver waveform design
The calculation of user spectrum efficiency is defined at the next pages

## Slide 10: Proposal (Evaluation metrics)
User spectrum efficiency is given by
Case 1:
where  denotes the number of correctly received bits by target user, T is the transmission time of the target user, and  =BWcarrier is the whole bandwidth including system guard band (see above figure).
Case 2:
where  denotes the number of correctly received bits by target user, T is is the transmission time of the target user, and  is the data bandwidth plus guard tone of the target UE plus guard tone.

## Slide 11: Proposal (Evaluation metrics)
User spectrum efficiency is given by
Case 3 and Case 4:
where  denotes the number of correctly received bits by target user, T is the transmission time of the target user, and  =BWUE1 is the data bandwidth plus guard tone of the target UE (see above figure)

## Slide 12: Proposal (Evaluation parameter for DL)
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD
System Bandwidth | 10 MHz
TTI length | 1 ms as baseline, other TTI length is FFS ( short TTI should be considered)
Subcarrier spacing | Single numerology case: 15KHz as baseline, Mixed numerology case: 15KHz, and the other subcarrier spacing FFS
Guard time interval | 4.7us (interval of LTE normal CP) as baseline, other interval is FFS
FFT size | 1024 for 15KHz subcarrier spacing
Data transmission bandwidth | Single numerology case: 50~55 PRBs for 15KHz subcarrier spacing Mixed numerology case: 4.5MHz bandwidth for target sub-band with 15KHz subcarrier spacing, with 1 PRB located at the edge of target sub-band for spectrum efficiency evaluation. 4.5MHz bandwidth for interfering sub-band with different subcarrier spacing (specific value FFS)
Guard tone number | 0~5, 10 subcarriers for the mixed numerology case
Number of Tx antenna ports | 1T1R, 4T4R
MIMO mode | TM3
Rank per UE | Fixed rank4 for 4T4R
MCS | Fixed. 16QAM: 1/2, 2/3; 64QAM: 1/2, 3/4;256 QAM: 1/2, 3/4
Control Overhead | No RS, PDCCH / EPDCCH / PSS / SSS / PBCH
Channel estimation | Ideal
Channel Model | ETU for 3km/h mobility (mandatory) EVA for 120km/h mobility (optional)
Table 1 Parameters for case 1 and case 2

## Slide 13: Proposal (Evaluation parameter for UL)
Table 2 Parameters for case 3 and case 4
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD
TTI length | 1 ms as baseline, other TTI length is FFS ( short TTI should be considered)
Subcarrier spacing | Single numerology case: 15KHz as baseline, Mixed numerology case: 15KHz, and the other subcarrier spacing is FFS
Guard time interval | 4.7us as baseline, other interval is FFS
FFT size | 1024 for 15KHz subcarrier spacing
Bandwidth per user (including target user and interfering user) | 720 KHz (48 Subcarriers allocated per user)
Number of uplink users | 3 (1 target user and 2 interfering users)
Power offset of the interfering user | 0 dB, 10 dB
Number of transmission antenna ports | 1T1R
MCS | Fixed. 16QAM: 1/2, 2/3; 64QAM: 1/2, 3/4
Control Overhead | No
Time offset of interfering user | Case 3 only: 0, 128, 512 samples (for 15 KHz subcarrier spacing)
Channel estimation | Ideal
Guard tone number | 0 ~5 ,10 Subcarriers
Channel Model | ETU for 3km/h mobility (mandatory) EVA for 120km/h mobility (optional)

## Slide 14: Other Evaluation detailed assumption
Proposal: It is FFS how to consider the RF nonlinearity in the aforementioned evaluation cases. Note that a common model of the RF nonlinearity needs to be agreed on first to allow accurate and fair comparison.
Observation 1: PA model is key to the usefulness of evaluation with PA non-linearity.
Observation 2: When LTE was introduced, RAN4 conducted evaluation on TX non-linearity. There were some PA models proposed for UE; for BS, realistic PAs were assumed together with clipping and DPD, however, without more details. In short, there was no commonly agreed-upon PA model for either UE or BS.