## Slide 1: WF on blocked CCA at UE
Samsung, Panasonic, ZTE, Nubia
R1-163576
3GPP TSG RAN WG1 Meeting #84b
Busan, Korea, 11th - 15th April 2016
Agenda item 7.3.1.1

## Slide 2: Background
It is required to distinguish the following three cases:
  Case 1 (missed UL grant); UL grant is failed to be received at UE
  Case 2 (blocked CCA); CCA is blocked at the UE successfully receiving UL grant
  Case 3 (bad UL link quality); UL data is failed to be received at eNB due to low SINR
Possible impacts from the ambiguity
  HARQ buffer management at eNB
  HARQ procedure and UL channel access

## Slide 3: Proposal
New indication of successful or failed LBT for PUSCH should be supported
  New UCI to indicate LBT result at CCA
  FFS: potential impacts of new indication
    UL HARQ (e.g. reduced HARQ buffer corruption)
    UL grant (e.g. fast UL grant for retransmission)
    UL channel access (e.g. LBT contention window adaptation)