## Slide 1
3GPP TSG RAN WG1 Meeting #84bis R1-163581
Busan, Korea, 11th - 15th April 2016
Agenda item: 7.3.3.2.2
WF on Hybrid CSI Reporting
Samsung, Alcatel-Lucent Shanghai Bell, CATT, Nokia, Qualcomm, LG Electronics, Beijing Xinwei, Interdigital, AT&T, China Telecom, Huawei, HiSilicon, CMCC, CATR

## Slide 2: Proposal
Specify the following enhancement on Rel.14 CSI reporting
One CSI process configured with 2 eMIMO-Types
  Each eMIMO-Type is associated with a set of K≥1 NZP CSI-RS resources

## Slide 3: Examples
Possible combinations to be considered:
  Other combination(s) are not precluded
First eMIMO-Type |  | Second eMIMO-Type | 
eMIMO-Type | CSI reporting content | eMIMO-Type | CSI reporting content
CLASS A | {i1, RI} or {i1} | CLASS B K2=1 | {RI, CQI, PMI} (*)
CLASS A | {i1, RI} | CLASS B K2>1 | {RI, CQI, PMI} , and optionally CRI
CLASS B K1>1 | CRI, and optionally i1 | CLASS B K2=1 | {RI, CQI, PMI}
CLASS B K1>1 | K1 independent CSI reports (**) | CLASS B K2=1 | {RI, CQI, PMI}
CLASS B K1=1 | PMI | CLASS B K2>1 | {RI, CQI, PMI}
(*) Possibility of removing RI in this report can be further discussed
(**) CSI for each resource contains at least a PMI – exact CSI content is FFS
Note: the CSI measurement can be based on partial antenna ports of Class A at the first stage.
  Note: CSI resource/CSI calculation for the 2nd eMIMO-Type can be conditioned on the last reported CSI for the 1st eMIMO-Type