## Slide 1: WF on SRS without PUSCH in eLAA
Huawei, HiSilicon, Qualcomm…
3GPP TSG RAN WG1 #84bis R1-163585
Busan, Korea
11th – 15th April 2016
Agenda item: 7.3.1.2
Document for decision

## Slide 2: Background
After the RAN1 84 meeting, there was an email discussion [84-15] on SRS without PUSCH in eLAA
The summary is in the contribution R1-162729

## Slide 3: Proposals
FFS: Periodic SRS without PUSCH is not supported in Rel-14 eLAA WI
A-periodic SRS without PUSCH is supported in Rel-14 eLAA WI
LBT for aperiodic SRS without PUSCH
  25us one-shot LBT within eNB MCOT;
  FFS 25us one-shot LBT or cat.4 LBT with high LBT priority class outside of eNB MCOT

## Slide 4: Proposal
SRS without PUSCH can be transmitted on UL symbols in the ending partial subframe, or in the 1st valid symbol of the UL subframe
DwPTS
SRS
SRS
PUSCH
UE1
UE2
SRS only
UE1

## Slide 5: Proposals
SRS without PUSCH can be triggered by dynamic signaling, for example
  Common DCI,
  Group DCI
  DL grants
  One or several of the above options may apply