## Slide 1: WF on Collision Handling for NB-IoT
Ericsson, …
R1-163589
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th -15th April 2016
Agenda item 7.2.1.3

## Slide 2: Proposal (1)
For PDSCH_SI carrying SI messages,
  When PDSCH_SI overlaps with subframes occupied by PBCH/PSS/SSS/SIB1, the PDSCH_SI is postponed to next subframe
  Subframes occupied by PDSCH_SI are treated as invalid subframe by NPDCCH and other PDSCH
    The NPDCCH and other PDSCH are postponed

## Slide 3: Proposal (2)
When NPDCCH/NPDSCH/NPUSCH repetition overlap with measurement gap
  The UE shall assume NPDCCH/NPDSCH/NPUSCH repetition in the overlapping subframe(s) is dropped, and the unavailable subframe(s) is counted in the repetition

## Slide 4: Proposal (3)
In case of collision between a scheduled NPUSCH transmission and NPRACH resources,
  NB-IoT UEs drop NPUSCH transmissions in the subframes that collide with the NPRACH resources
UEs in lower coverage treat NPRACH opportunities that collide with NPRACH opportunities of higher coverage level(es) as invalid.
  UEs only use valid NPRACH opportunities for Msg1 transmission