## Slide 1: WF on valid/invalid subframe configurations and MBSFN subframe configuration
Panasonic, ZTE, Mediatek
R1-163590
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11-15 April, 2016
Agenda item 7.2.1.3

## Slide 2: Background
    Valid/invalid subframe configuration is important for forward compatibility reasons.
      Standalone/guardband of NB-IoT may be located in NR bandwidth.
    Subframe 0,4,5,9 are fully utilized in NB-IoT in anchor carrier.
      In non-anchor carrier, these subframes may be configured as invalid.
    The usage of MBSFN subframe usage in NB-IoT is unclear.

## Slide 3: Proposals
    Valid subframe configuration
      Valid subframe configuration are optionally bit-map configured over 10ms or 40ms for standalone/guardband/inband by NB-SIB1.
      In the subframes that contain PSS/SSS/PBCH/NB-SIB1 in the carrier that contain PSS/SSS/PBCH/NB-SIB1
        these subframes are invalid subframes i.e. to postpone the transmission regardless of the signalling.
      For the remaining subframes,
        If no bit-map is provided, these subframes are valid subframes
        Otherwise, to follow the signalling.
      Discussion options for valid subframe configurations. We propose option 1.
        Option 1: One-bit map of 10 or 40 bits common to all carriers in a cell.
        Option 2: One-bit map of 6 or 24 bits common to all carriers in a cell. Only MBSFN configurable subframes are signaled.
        Option 3: Two bit map for anchor and non-anchor possibility. 6 or 24 bits to anchor carrier. 10 or 40 bits for non-anchor.
        Option 4: Multiple bit map for each carrier possibility. 6 or 24 bits to anchor carrier. 10 or 40 bits for non-anchor.
    NB-IoT UE may assume any MBSFN subframe is not configured. (= The network shall configure MBSFN subframes as invalid subframes)