## Slide 1: WF on UL Narrowband DMRS
Ericsson, …..,
R1-163591
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.2.1.2.5

## Slide 2: Background
Some agreements for multi-tone:
DMRS symbol locations for multitone are the same as for LTE
For 3-tone case, 16 base sequences are provided (new sequences, not truncated versions of the 6-tone sequences)
For 6-tone case, 16 base sequences are provided
Define 3 cyclic shifts for the 3-tone case and 4 for the 6-tone case
No CSs for 12-tone case
Cyclic shifts are indicated by SIB and not indicated in DCI
No OCC
Sequences are QPSK in frequency domain

## Slide 3: Proposal 1
16 base sequences for 3-tone case are defined as
with
m | (0),(1),(2) |  | 
0 | 1 | -3 | -3
1 | 1 | -3 | -1
2 | 1 | -3 | 1
3 | 1 | -3 | 3
4 | 1 | -1 | -3
5 | 1 | -1 | -1
6 | 1 | -1 | 1
7 | 1 | -1 | 3
8 | 1 | 1 | -3
9 | 1 | 1 | -1
10 | 1 | 1 | 1
11 | 1 | 1 | 3
12 | 1 | 3 | -3
13 | 1 | 3 | -1
14 | 1 | 3 | 1
15 | 1 | 3 | 3

## Slide 4: Proposal 2
For each of the 3-tone base DMRS sequence, three cyclic shifts are defined as
,
where is a base sequence, , and is the cyclic shift .

## Slide 5: Proposal 3
For each of the 6-tone base DMRS sequence, three cyclic shifts are defined as
,
where is a base sequence, , and is the cyclic shift .

## Slide 6: Proposed Working Assumption
16 base sequences for 6-tone case are defined as with
Alt1
m | (0), (1), (2), (3), (4), (5), |  |  |  |  | 
0 | 1 | 1 | 1 | 1 | 3 | -3
1 | 1 | 1 | -1 | -3 | -3 | 3
2 | 1 | 1 | 3 | 1 | -3 | 3
3 | 1 | -1 | -1 | -1 | 1 | -3
4 | 1 | -1 | 3 | -3 | -1 | -1
5 | 1 | 3 | 1 | -1 | -1 | 3
6 | 1 | -3 | -3 | 1 | 3 | 1
7 | -1 | -1 | 1 | -3 | -3 | -1
8 | -1 | -1 | -1 | 3 | -3 | -1
9 | 3 | -1 | 1 | -3 | -3 | 3
10 | 3 | -1 | 3 | -3 | -1 | 1
11 | 3 | 3 | -3 | -3 | -3 | -1
12 | 3 | -3 | 3 | -1 | 3 | 3
13 | -3 | 1 | 3 | 1 | -3 | -1
14 | -3 | 1 | -3 | 3 | -3 | -1
15 | -3 | 3 | -3 | 1 | 1 | -3
Maximum pairwise cross-correlation: 0.7454
Mean cross-correlation: 0.3652
Median cross-correlation: 0.3592
Sample std: 0.1828

## Slide 7: Proposed Working Assumption
Alt2
  Given in R1-163424

## Slide 8: Proposed DM-RS multi-tone evaluation methods
First, prioritize cross-correlation
  Preferred maximum pair-wise cross-correlation to be between 0.7 to 0.8
Second, check the cross-correlation between length-6 and length-3, 12 DM-RS sequences.
Third, check CM or PAPR according to
  Alt1, Case 2 on next slide
  Alt2, Case 4 on next slide compare to data only without DM-RS sequences
  CM is calculated as

## Slide 9: Cases of CM or PAPR evaluations