## Slide 1: WF on NB-PRACH power ramping
ZTE, HW, Hisilicon, [Ericsson , Sierra wireless]…
R1-163595
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th - 15th April 2016
Agenda item 7.2.1.2.4

## Slide 2: Proposal
It is ran1 understanding that the following power ramping equation can be reused for NB-PRACH but one item (– 10*log10(numRepetitionPerPreambleAttempt) to adjust repetition’s effect need to be added
  Set PREAMBLE_RECEIVED_TARGET_POWER to preambleInitialReceivedTargetPower + DELTA_PREAMBLE + (PREAMBLE_TRANSMISSION_COUNTER – 1) * powerRampingStep – 10*log10(numRepetitionPerPreambleAttempt)
    DELTA_PREAMBLE is set to 0
Inform RAN2 about this RAN1 understanding