## Slide 1: 15 KHz and 17.5 KHz Based Numerology Comparison
Qualcomm Incorporated, ZTE
R1-163620
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11 – 15, 2016
Agenda Item: 8.1.5

## Slide 2: Scalable numerology comparison
 | LTE numerology based family (SCS = 15kHz) | 2N based numerology family (e.g. SCS = 17.5kHz)
Forward compatibility |  | 
Numerology for typical deployment scenarios | SCS = 15kHz, 30kHz or 60kHz, … CP = 4.7us, 2.35us, 1.18us | SCS = 17.5kHz, 35kHz or 70kHz, … CP = 5.4us, 2.7us, 1.3us
TTI scaling down via numerology scaling | SCS scaling to achieve TTI scaling | SCS scaling to achieve TTI scaling
TTI scaling down via reducing number of symbols | Fractional symbol (efficiency loss) Non-uniform TTI (non-uniform latency) | Scalable with pow of 2 symbols per TTI
Long CP support | LTE ECP option (large overhead) | Scalable long CP symbol (same overhead as short CP)
Legacy coexistence |  | 
NB-IOT Coexistence | Guardband overhead | Guardband overhead
LTE TDD Coexistence | TDM or FDM: considering NR SF structure | TDM or FDM: considering NR SF structure

## Slide 3: Scalable Numerology Family Comparison
Common scalable numerology family:
  One base subcarrier spacing Δf0
  Derive other subcarrier spacing values in the family by power of 2 scaling
Subcarrier spacing Δfk = Δf0*2k,
CPk = CP0/2k,
Option 1 (LTE based numerology):
  14*2k symbols per ms
  Δf0 = 15kHz
Option 2 (2N symbol per ms numerology):
  16*2k symbols per ms
  Δf0 = 17.5kHz (not precluding other values, e.g. around 17 kHz)
where k is an integer, where k could be positive or negative or 0

## Slide 4: Scalable TTI design via reducing number of symbols
Comparison of scalable 17.5kHz numerology vs. 15kHz numerology
2N numerology family (e.g. SCS = 17.5 KHz) scaling down number of symbols:
  Low latency with CP robustness
  Uniform scaled TTI duration to achieve uniform latency design
LTE numerology family (SCS = 15 KHz):
  Fractional symbol per TTI (efficiency loss)
  Non-uniform TTI duration (non-scalable and non-uniform latency concern)
Notes: 350km/hr at 600Hz Doppler is under consideration in 3GPP

## Slide 5: Scalable long CP design considerations
Comparison of two ways scaling to long CP duration:
17.5kHz scalable numerology,
  SCS = 8.75kHz, 8 symbols per slot, CP duration = 10.7us, CP overhead = 8.57% for large cell
  SCS = 4.375kHz, 4 symbols per slot, CP duration = 21.4us, CP overhead = 8.57% for MBSFN
15kHz numerology, use LTE ECP, 6 symbols per slot, CP duration = 16.7us, CP overhead = 20%
Link-level/system-level evaluation of CP duration and Doppler sensitivity evaluation
Notes: 350km/hr at 600Hz Doppler is under consideration in 3GPP

## Slide 6: NB-IOT coexistence in adjacent carrier
Comparison overhead of 15kHz vs. 17.5kHz coexistence with 15kHz spacing NB-IOT
  15 KHz NR fully sync-ed to 15kHz NB-IOT  0 guard tone coexistence
  15 KHz NR async to NB-IOT  ~10% guard overhead
  15 KHz NR adjacent to 3.75kHz NB-IOT  ~10% guard overhead
  17.5 KHz NR async to NB-IOT  ~10% guard overhead
Comparison of NR 30kHz vs. NR 35kHz coexistence with 15kHz spacing NB-IOT
  Same, ~10% guard overhead
Comparison of NR 60kHz vs. NR 70kHz coexistence with 15kHz spacing NB-IOT
  Same, ~10% guard overhead
Notes: 350km/hr at 600Hz Doppler is under consideration in 3GPP

## Slide 7: LTE TDD coexistence consideration
Co-channel TDM coexistence:
  NR operating in LTE TDD blank SFs (e.g. reserved TDD UL subframes)
  Only SF level alignment is sufficient, no need for numerology alignment.
   No difference between 15 KHz and 17.5 KHz
Adjacent carrier coexistence:
  If considering new subframe structure, e.g., low latency turn around, DL/UL duplexing direction will be fundamentally different from LTE DL-UL configuration
     No difference between 15 KHz and 17.5 KHz
  Flexible configuration of NR subframe structure to match LTE DL-UL configuration
     No need for exact chip-level alignment between NR and LTE TDD
    Additional guard period difference in special subframe:
       15 KHz, exact guard period as LTE
       17.5 KHz, slightly longer guard period with additional overhead < 1 OFDM symbol / 5ms, i.e., 1.25%
Notes: 350km/hr at 600Hz Doppler is under consideration in 3GPP