## Slide 1: Way Forward on V2V PC5 timing
3GPP TSG RAN WG1 Meeting #84b R1-163629
Busan, Korea, 11th - 15th April 2016
Agenda Item: 7.3.2.4
Huawei, HiSilicon, ITRI, OPPO, CATR, Potevio, NEC, …

## Slide 2: Background
  There are agreements on the V2V sync:
  eNB instructs vehicle UE to prioritize either eNB-based synchronization or GNSS or GNSS-equivalent at least when the eNB is in the carrier where the vehicle UE operates on PC5 V2V
  GNSS or GNSS-equivalent is at the highest priority of synchronization source for time and frequency when the vehicle UE directly receives GNSS or GNSS-equivalent with sufficient reliability and the UE does not detect any cell in any carrier.

## Slide 3: Background
Observation:
  The timing of PC5 for V2V on the dedicated carrier can be decoupled from the eNB timing.
  It is beneficial for V2V PC5 to use a universal timing when the network is asynchronous.
    Reduce the packet missing or avoid additional time delay when multiple different timings received by a UE under the asynchronous network
  Note: the dedicated carrier means the eNB is not in the carrier where the vehicle UE operates on PC5 V2V

## Slide 4: Proposal
  A PC5 V2V uses a UTC timing when the eNB is not in the carrier where the vehicle UE operates on PC5 V2V
      PC5 V2V Frame Number (VFN) is derived from the UTC timing
        FFS: how to derive the VFN