## Slide 1: WF on modeling of time-varying angles
Ericsson, ...
3GPP TSG RAN1 #84bis
Busan, Korea, April 11 - 15, 2016
Agenda Item: 8.2.2
R1-163636

## Slide 2: Background
Introduction of spatial consistency modeling will result in time-varying angles of departure and arrival leading to time-varying Doppler frequencies
Non-linear UE motion will also lead to time-varying Doppler frequencies
In R1-163246 it was observed that the equation in 36.873 for generating channel coefficients is ill-suited to handle time-varying Doppler frequencies
  Doppler shifts become unbounded as simulation time increases

## Slide 3: Background
A solution was proposed in R1-163246 where the channel coefficient equation is updated
  The factor in equation (7.21) is changed into where the phase shift at time is established as an anchor point and an incremental phase shift is applied.
  The anchor point should be updated sufficiently often so that
  If the Doppler frequency is time-independent the original equation is obtained

## Slide 4: Proposal
Proposal 1: Replace the factor with in the channel coefficient equation
  The phase shift at time is established as an anchor point and an incremental phase shift is applied
  The anchor point should be updated sufficiently often so that
Proposal 2: Proposal 1 needs only to be considered in case the Doppler frequencies are time-varying. This could be due to:
  Non-linear UE movement
  Time-varying angles of arrival due to spatial consistency modeling