## Slide 1: WF on RMa model
Ericsson, …
R1-163640
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th - 15th April 2016
Agenda Item: 8.2.1

## Slide 2: Background
In the evaluation discussions, a Rural Macro scenario has been proposed
  For evaluations below 6 GHz
3GPP has no Rural channel model, but IMT-Adv has a 2D model in ITU-R M.2135

## Slide 3: Proposal
Adopt the ITU-R M.2135 Rural Macro model for rural macrocell simulations
Enhance the RMa model to 3D using elevation parameters taken from the 5G UMa model
Tuning of the elevation parameters is FFS
  For example, the elevation angle spread is expected to be lower in rural scenarios
Capture the model in the TR by reference to M.2135 + a table with the additional parameters
  Put square brackets around the ”UMa” parameters pending further tuning