## Slide 1: WF on UL 256QAM MCS table
Huawei, HiSilicon, CATR, ZTE, …
R1-163652
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.3.8

## Slide 2: Proposals
The MCS modulation switching point between 64QAM and 256QAM for the PUSCH is
  The modulation corresponding to TBS index 29 is 64QAM;
  The modulation corresponding to TBS index 30 and higher is 256QAM.
Entries in PUSCH MCS table supporting 256QAM is indicated by 5 bits.
The number of PUSCH MCS entries to support 256QAM is down-selected between
  Alt 1: 6
  Alt 2: 5