## Slide 1: WF on Scheduling Collision
Sony, Intel, MediaTek, Sequans, Sierra Wireless, Virtuosys, CATT, Panasonic, Huawei, HiSilicon, Neul, ZTE, Samsung
R1-163658
3GPP TSG RAN WG1 84bis
Busan, Korea 11th - 15th April 2016
Agenda item 7.2.1.1.1

## Slide 2: Background (1)
After NB-PDCCH 1 schedules a data channel, if another NB-PDCCH 2 schedules another data channel between NB-PDCCH 1 and the corresponding data channel a collision can occur.

## Slide 3: Proposal
An NB-IoT UE that has received a grant from an NB-PDCCH is not required to monitor NB-PDCCH for any further DL or UL grant during the time period between the end of the NB-PDCCH that schedules the grant and the start of the corresponding NB-PDSCH or NB-PUSCH transmission