## Slide 1: WF on UL 256 QAM Design
Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, …
R1-163690
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.3.8

## Slide 2: Proposal
No new TBS index is introduced to support UL 256QAM.
The number of bits for the MCS field in the DCI message to support UL 256QAM is 5 bits.
The minimum TBS index for 16QAM is 11.
The minimum TBS index for 64QAM is 20.
The minimum TBS index for 256QAM is 30.
3 entries are reserved for retransmissions.