## Slide 1: Way forward on UL LBT For: Decision AI: 7.3.1.5
Intel,…
3GPP TSG-RAN WG1 #84-bis R1-163707
Busan, Korea, Apr 11-15, 2016

## Slide 2: Background
In the email discussion during Release 13 LAA WI, the following agreements on UL LBT were made:
Agreement:
For self-carrier scheduling, the following UL LBT candidate procedures should be considered
  A CCA duration of at least 25 us before the transmission burst
    The sensing duration in a CCA slot can be less than the CCA slot duration
  A category 4 LBT scheme with a defer period of 25 µs including a defer duration of 16 us followed by one CCA slot, and a maximum contention window size chosen from X={3, 4, 5, 6, 7},
    FFS: The random backoff counter is generated at the eNB and is signaled to the UE
    FFS: When a UL grant is subject to LBT with a new random counter, the UL transmissions scheduled by the UL grant also uses a new random counter (previous counter is discarded) irrespective of prior success/failure in accessing the channel.
    The UL maximum contention window size should be smaller than for DL category 4 LBT
    Note that X = 7 can be revisited later after DL LBT discussions, if necessary
  FFS: Energy detection threshold used for UL LBT

## Slide 3: Background
  Agreement:
  For cross-carrier scheduling, when an LBT operation is performed on the SCell to send a grant on another Cell, the UL LBT procedure is the same as that for self-carrier scheduling.
  For cross-carrier scheduling, when an LBT operation is not performed on the SCell, one or more of the following UL LBT procedures should be supported
    A CCA duration of at least 25 us before the transmission burst
      The sensing duration can be less than the CCA duration
    A category 4 LBT scheme with a defer period of 25 µs including a defer duration of 16 us followed by one CCA slot,
      FFS: The random backoff counter is generated at the eNB and is signalled to the UE
      FFS: Whether the UL maximum contention window size can be smaller than that for DL category 4 LBT
      FFS: Whether the UL maximum contention window size should be greater than that for self-carrier scheduled UL
    FFS: Energy detection threshold used for UL LBT

## Slide 4: Proposal
  For cross-carrier scheduling, when an LBT operation is not performed on the LAA SCell to send a grant on another licensed Cell, Cat-4 LBT is used for UL LBT.
    FFS: Whether the UL maximum contention window size can be smaller than that for DL category 4 LBT
  Energy detection threshold used for UL LBT for both self-carrier and cross-carrier scheduling is based on the energy detection threshold rule for DL LBT.
  LBT for UL grant only transmission by eNB follows Cat-4 LBT with high priority.
    FFS: the priority class to be used for UL grant only transmission.