## Slide 1: WF on Numerology Comparison
Qualcomm Incorporated, ZTE, OPPO, ETRI
R1-163715
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11 – 15, 2016
Agenda Item: 8.1.5

## Slide 2: Summary
Use analysis and numerical quantification to compare the prons and cons of 15kHz family and 2^N symbol family (e.g., 17.5kHz SCS)
  Impact on performance and processing complexity
  Impact on legacy coexistence

## Slide 3: Scalable numerology 15KHz vs. 2N family forward compatibility study
Modular and scalability design comparison (analysis + simulation)
  Data burst/symbol boundary alignment and scalability impact analysis
  Modular vs. non-modular design complexity analysis
  Scaling SCS of 15KHz family vs. reducing the number of symbols scaling of 17.5KHz family performance comparison
Link-level numerology comparison (simulation)
  Identify numerology scaling for typical deployment scenarios for evaluation
  Performance evaluation over 3GPP channel models: scaled EPA/EVA/ETU (for diff deployment scenarios)
  Link-level evaluation of long CP (simulation and analysis)
  15KHz family based on LTE ECP vs. 17.5KHz scaled SCS (vs. other alternatives)
  3GPP long DS channel model performance evaluation

## Slide 4: Example of Modular vs. non-modular design analysis
URLLC short data burst design
Modular design:
Non-modular design:
Data burst boundary of 2-symb vs. 3-symb misaligned, not self-contained

## Slide 5: Legacy coexistence evaluation
NB-IOT coexistence evaluation (simulation/analysis)
  Guardband overhead comparison
LTE TDD Coexistence (analysis):
  Additional GP overhead quantification
Sampling Rate Complexity (analysis)

## Slide 6: Scalable numerology: 15KHz vs. 2N family comparison
subcarrier spacing: Δfk = Δf0*2k,
CPk = CP0/2k
To consider numerology within power of 2 scaling family
  15KHz scaling family:
    SCS = 15KHz, 30KHz or 60KHz, …
    CP = 4.7us, 2.35us, 1.18us
  2N-symbol scaling family:
    SCS = 17.5KHz, 35KHz or 70KHz, …
    CP = 5.4us, 2.7us, 1.3us
  Considering the CP difference is relatively small, WF to narrow down a set of k options first and keep the discussion of 15KHz vs. 2N-symbol open pending evaluation