## Slide 1: WF on 3-Tone NPUSCH DMRS
Qualcomm, Samsung, Ericsson, ZTE, Panasonic, Nokia, Sony, LG, Intel
R1-163734
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.2.1.2.5

## Slide 2: Background
All the 16 possible distinguish sequences for 3-tone case are included.
Some of them have very large CM.
  The maximal CM of any 3-tone SC-OFDM symbol is 3.5 dB.
  The maximal CM of the 3-tone DMRS sequence is 4.6 dB.

## Slide 3: Proposal
14 base sequences for 3-tone case are defined as
with
m | (0),(1),(2) |  | 
0 | 1 | -3 | -3
1 | 1 | -3 | -1
2 | 1 | -3 | 1
3 | 1 | -3 | 3
4 | 1 | -1 | -3
5 | 1 | -1 | -1
6 | 1 | -1 | 3
7 | 1 | 1 | -3
8 | 1 | 1 | -1
9 | 1 | 1 | 3
10 | 1 | 3 | -3
11 | 1 | 3 | -1
12 | 1 | 3 | 1
13 | 1 | 3 | 3