## Slide 1: WF on scrambling sequence design for NB-SSS
Huawei, HiSilicon, Intel Corporation
R1-163735
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11-15 April, 2016
Agenda item 7.2.1.1.4

## Slide 2: Background
NB-SSS periodicity is 20ms
The following information is indicated by the NB-SSS:
  One of 504 PCIDs
  80ms boundary (4 values)
NB-SSS sequence is composed of a length-131 frequency-domain ZC sequence and a binary scrambling sequence
  Root indices {3..128}
PCID is indicated by combination of ZC root index and a binary scrambling sequence
80ms boundary is indicated by the one of 4 time-domain cyclic shifts, {0, 33, 66, 99}
The binary scrambling sequence is a Hadamard sequence
  Working assumption (from R1-163442), to be confirmed on Wed if no significant problems are identified:

## Slide 3: Observations
    Time domain cyclic shift is done according to the frequency domain implementation described in R1-162976
    Alt 1:
      Set of Hadamard indices: {0,31,63,127}
    Alt 2:
      Set of Hadamard indices: {0,5,10,15}

## Slide 4: Observations
    Synchronized BS
Ssync | 90% | 99% | 99.90% | 100%
Alt1 | 0.122 | 0.172 | 0.182 | 0.182
Alt2 | 0.122 | 0.142 | 0.153 | 0.153

## Slide 5: Observations
    Asynchronized BS
Async | 90% | 99% | 99.90% | 100%
Alt1 | 0.204 | 0.249 | 0.370 | 0.576
Alt2 | 0.1913 | 0.2339 | 0.5119 | 0.7387

## Slide 6: Proposal1
    NB-SSS sequence is generated according to R1-162976 with following correction:

## Slide 7: Proposal2
The binary scrambling sequence for NB-SSS is a Hadamard sequence generated as