## Slide 1: WF on Remaining Issues for DL Transmission Gap of NB-IoT
Ericsson, ….
R1-163743
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th -15th April 2016
Agenda item 7.2.1.1.1

## Slide 2: Background (1)
Agreement:
  For each configuration, the cycle starts with transmission period followed by the subframes for the gaps
  The gap configuration is optional; if not configured it means there is no gap
  DL transmission gap does not apply to SIB transmission.
  Gaps configuration is applied for both NPDCCH CSS for paging and NPDSCH carrying the paging message
    The same configuration is used for paging NPDCCH and NPDSCH as that of other DL transmission
    For paging, R_NPDCCH_max refers to Rmax of paging CSS configured by eNB

## Slide 3: Background (2)
Agreement:
  Starting point of gap period (SFN=0, sf=0)
  {Gap starting point periodicity, Gap size} are
    Alt 2: signaled separately
      2 bits each
  X1 is 2 bits
    {32, 64, 128, 256}
  Gap starting point periodicity and gap size are
    On an absolute number of subframes

## Slide 4: Proposal (1)
When DL transmission gap is configured, each cycle starts with subframe (nf, ns) where Tg is the Gap starting point periodicity, and
When a cycle cross over (SFN=0, sf=0)
  If the DL transmission part crosses over, both DL transmission part and gap part of the cycle are skipped
  If the DL transmission part does not crosses over, and the gap part crosses over, then: only the gap part of the cycle is skipped, DL transmission part is kept

## Slide 5: Proposal (2)
Value set for {Gap starting point periodicity, Gap size} is defined using one of the alternatives below:
  Alt 1. As a function of X1
    Value set for Gap starting point periodicity is P subframes, where P{X1, X1*2, X1*4, X1*8}
    Value set for Gap size is G subframes, where G{X1/4, X1/2, X1, X1*2}
  Alt 2. Not as a function of X1
    Value set for Gap starting point periodicity is P subframes, where P{64, 128, 256, 512}
    Value set for Gap size is G subframes, where G{16, 32, 64, 128}