## Slide 1: WF on remaining details of NPDCCH starting subframes
Huawei, HiSilicon, Intel, MediaTek
R1-163801
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11-15, 2016
Agenda item 7.2.1.1.1

## Slide 2: Background
Agreements on starting subframes:
The search space starting subframe reuses the principle of eMTC
  The period reuse the principles from eMTC
    T=R*G, G values to be determined
    An additional offset on the value of T may be considered
Postpone NPDCCH repetitions that overlap with transmission gap
G={1.5, 2, 4, 8, 16, 32, 48, 64}
eNB only configures values that result in T>=4
T=Rmax*G

## Slide 3: Background
RAN1 needs to clarify the following points:
Is G configured separately for UE-SS and CSS for RAR/Msg3re-tx/Msg4?
Assuming “yes” to #2, wrt CSS for RAR/Msg3re-tx/Msg4, is G:
  Cell specific only; or
  Cell specific and NPRACH resource specific

## Slide 4: Proposals
G is configured separately for UE-SS and CSS for RAR/Msg3re-tx/Msg4
For CSS for RAR/Msg3re-tx/Msg4, G is configured per-cell per NPRACH resource